## Slide 1
Design Variation + Performance Map Using SimericsMP
Python Script Solution

## Slide 2: Objectives + Prerequisites
Objectives:
  Instantly create multiple CFturbo designs with varying design parameters for study of optimization and sensitivity (slide #3)
  Streamline the workflow that is running multiple simulations using SimericsMP to construct a performance map (slide #19)
Prerequisites:
  Cfturbo
    https://cfturbo.com/software/download
  SimericsMP
  Python
    https://www.python.org/downloads/
  Text Editor (Visual Studio Code)
    https://code.visualstudio.com/download
    Python Extension
  Microsoft Excel
  CFturbo Inc. Python Scripts
    https://github.com/sandschristopher/master

## Slide 3: Design Variation + Performance Map Using SMP (A + B)
General Workflow:
  Run steady-state simulations for each design variation
  Analyze performance of each design variable to find optimal design
  Run a full performance map for the optimal design
General Outline – Design Variation:
  Create and Prepare Project Folder
  Select Design Variation Parameters/Export to SimericsMP
  User Modification of master.cftconf
  Run master.py within Visual Studio Code
  Fill in Design Parameter Values in .csv
  Open Results .csv File for Post-Processing

## Slide 4: I. Create and Prepare Project Folder
Create and name a project folder accordingly (e.g. axial-fan_v1)
Download the CFturbo python scripts from github repository and place within project folder:
  master.cftconf
  master.py
  modify_spro.py
Ensure the Cfturbo Design File (project_name.cft) is also in the project folder, both with the same name!

## Slide 5: II. Select Design Variation Parameters/Export to SMP
After the design process within CFturbo, select Batch mode/optimization under the Project tab
Under the Parameters tab, check the box corresponding to each design parameter you wish to vary.

## Slide 6: II. Select Design Variation Parameters/Export to SMP (cont.)
Under the Export actions tab:
  Within the Export interfaces window, open CFD and highlight Simerics
  Within the Components window, check the box corresponding to the design component you wish to include in the simulation geometry
  Select Directory and assign the project folder

## Slide 7: II. Select Design Variation Parameters/Export to SMP (cont.)
Within the Settings window, ensure Export all files is selected in the dropdown menu
Select Solver and choose the Steady solver type from the dropdown menu
Denote the base file name with the marker that suggests the steady solver type (_steady)

## Slide 8: II. Select Design Variation Parameters/Export to SMP (cont.)
Click Add
Click Save as... and save the CFturbo Batch File to the project folder with the marker that suggests the steady solver type (e.g. axial-fan_v1_steady.cft-batch)

## Slide 9: II. Select Design Variation Parameters/Export to SMP (cont.)
If transient simulation results are desired, then repeat:
  Within the Settings window, ensure Export all files is selected in the dropdown menu
  Select Solver and choose the Transient solver type from the dropdown menu
  Denote the base file name with the marker that suggests the transient solver type (_transient)

## Slide 10: II. Select Design Variation Parameters/Export to SMP (cont.)
Click Add
Click Save as... and save the CFturbo Batch File to the project folder with the marker that suggests the transient solver type (e.g. axial-fan_v1_transient.cft-batch)

## Slide 11: III. User Modification of master.cftconf
Open the project folder within the text editor and select the master.cftconf file

## Slide 12: III. User Modification of master.cftconf (Cont.)
Under [Project]:
  Assign the project name to project_name
    This should be consistent with the base file name and project folder named previously
Under [DesignVariation]:
  Set run_design_variation_bool to True
  Set cft_version to the CFturbo version being used (e.g. 2022.2.2)

## Slide 13: III. User Modification of master.cftconf (Cont.)
Under [Simerics]:
  Set run_simerics_bool to True
  Set simerics_version to either SimericsMP or SimericsMP+
Under [Steady]:
  Set avg_window to an appropriate integer value for averaging of iterations
Under [Transient]:
  Set run_transient_bool to True or False
  Set avg_window to an appropriate integer value for averaging of timesteps

## Slide 14: III. User Modification of master.cftconf (Cont.)
Under [PerformanceMap]:
  Set run_performance_map_bool to False

## Slide 15: IV. Run master.py in VS Code
Within the text editor, open terminal and run the master.py
If using Visual Studio Code:
  Select Terminal > New Terminal
  Within the Terminal type python master.py and click Enter on keyboard
  Use the pip3 install [library] command to install the necessary libraries
The user is prompted to input information regarding subsecting control volumes within the flow path:
  How many subsecting CVs they wish to examine
  The number associated with the initial/final component of each subsecting CV

## Slide 16: V. Fill in Design Parameter Values in .csv
Once python master.py is executed, the user will be prompted to fill a resultant .csv file with respective values
Once done filling the .csv file with design parameter values, return to the Terminal and press <Enter>

## Slide 17: VI. Open Results .csv File for Post-Processing
Manual convergence control can be analyzed simultaneously within the SimericsMP application
Wait for the program to finish
Within File Explorer, open the resultant .csv files
The averaged results of performance characteristics for each Cfturbo design are displayed
  The user should examine the performance of each design and run the following performance map script for the optimal design
Note: Within the Terminal, a “Fatal Error (MGI)“ message might be prompted... Ignore this!

## Slide 18: Performance Map Using SMP (B Only)
General Outline - Performance Map:
  Create and Prepare Project Folder
  CFturbo Design Export to SimericsMP
  User Modification of master.cftconf
  Run master.py within Visual Studio Code
  Open Results .csv File for Post-Processing

## Slide 19: I. Create and Prepare Project Folder
Create and name a project folder accordingly
Download the CFturbo python scripts from github repository and place within project folder:
  master.cftconf
  master.py
  modify_spro.py

## Slide 20: II. CFturbo Design Export to SimericsMP
Open the optimal design Cfturbo Design file, select Export
Under Export interfaces open CFD and select Simerics
Under Components check the design parts to include in the simulations geometry

## Slide 21: II. CFturbo Design Export to SimericsMP (Cont.)
Under Settings, ensure Export all files is selected in the dropdown menu
Select Solver and choose the Steady solver type from the dropdown menu
  steady simulations are necessary to run transient simulations
Denote the base file name with the marker that suggests the steady solver type (_steady)

## Slide 22: II. CFturbo Design Export to SimericsMP (Cont.)
Assign the project folder to the Directory
Select Export
Note: If Transient simulation results are desired, Steady simulations should be run

## Slide 23: II. CFturbo Design Export to SimericsMP (Cont.)
If transient simulation results are desired, then repeat:
  Under Settings, ensure Export all files is selected in the dropdown menu
  Select Solver and choose the Transient solver type from the dropdown menu
    steady simulations are necessary to run transient simulations
  Denote the base file name with the marker that suggests the transient solver type (_transient)

## Slide 24: II. CFturbo Design Export to SimericsMP (Cont.)
Assign the project folder to the Directory
Select Export
Note: If Transient simulation results are desired, Steady simulations should be run

## Slide 25: III. User Modification of master.cftconf
Open the project folder within the text editor and select the master.cftconf file

## Slide 26: III. User Modification of master.cftconf (Cont.)
Under [Project]:
  Assign the project name to project_name
    This should be consistent with the base file name and project folder named previously, or be the file name of the optimal design determined from design variation
Under [DesignVariation]:
  Set run_design_variation_bool to False
  Set cft_version to the CFturbo version being used (e.g. 2022.2.2)

## Slide 27: III. User Modification of master.cftconf (Cont.)
Under [Simerics]:
  Set run_simerics_bool to True
  Set simerics_version to either SimericsMP or SimericsMP+
Under [Steady]:
  Set avg_window to an appropriate integer value for averaging of iterations
Under [Transient]:
  Set run_transient_bool to True or False
  Set avg_window to an appropriate integer value for averaging of timesteps

## Slide 28: III. User Modification of master.cftconf (Cont.)
Under [PerformanceMap]:
  Set run_performance_map_bool to True
  Set rpm_type to relative or absolute
  Assign the respective values to rpm_values
  Set flowrate_type to relative or absolute
  Assign the respective values to flowrate_values
Note: If using absolute values for flowrate_values, the values must be in cubic meters per second or kilograms per second; flowrates can be either volumetric or mass but must be consistent with that of the Design Point in the Global setup within CFturbo

## Slide 29: IV. Run master.py in VS Code
Within the text editor, open terminal and run the master.py
If using Visual Studio Code:
  Select Terminal > New Terminal
  Within the Terminal type python master.py and click Enter on keyboard
  Use the pip3 install [library] command to install the necessary libraries
The user is prompted to input information regarding subsecting control volumes within the flow path:
  How many subsecting CVs they wish to examine
  The number associated with the initial/final component of each subsecting CV

## Slide 30: V. Open Results .csv File for Post-Processing
Wait for the program to finish
Within File Explorer, open the resultant .csv files
The averaged results of performance characteristics for each design point are displayed