## Slide 1
Design Variation + Performance Map Using SimericsMP
Python Script Solution

## Slide 2: Design Variation + Performance Map Using SMP
Objectives:
  Instantly create multiple CFturbo designs with varying design parameters for study of optimization and sensitivity.
  Streamline the workflow that is running multiple simulations using SimericsMP to construct a performance map.
Prerequisites:
  Cfturbo
    https://cfturbo.com/software/download
  SimericsMP
  Python (3.10.1)
    https://www.python.org/downloads/
  Text Editor (Visual Studio Code)
    https://code.visualstudio.com/download
    Python Extension
  Microsoft Excel
  CFturbo Inc. Python Scripts
    https://github.com/sandschristopher/master

## Slide 3: Design Variation + Performance Map Using SMP
General Outline – Design Variation:
  Create and Prepare Project Folder
  Select Design Variation Parameters/Export to SimericsMP
  User Modification of master.cftconf
  Run master.py within Visual Studio Code
  Fill in Design Parameter Values in .csv
  Open Results .csv File for Post-Processing

## Slide 4: I. Create and Prepare Project Folder
Create and name a project folder accordingly
Download the CFturbo python scripts from github repository and place within project folder:
  master.cftconf
  master.py
  modify_spro.py

## Slide 5: II. Select Design Variation Parameters/Export to SMP
After the design process within CFturbo, select Batch mode/optimization under the Project tab
Under the Parameters tab, check the box corresponding to each design parameter you wish to vary.

## Slide 6: II. Select Design Variation Parameters/Export to SMP (cont.)
Under the Export actions tab:
  Within the Export interfaces window, open CFD and highlight Simerics
  Within the Components window, check the box corresponding to the design component you wish to include in the simulation geometry

## Slide 7: II. Select Design Variation Parameters/Export to SMP (cont.)
Within the Settings window, ensure Export all files is selected in the dropdown menu
Select Solver and choose the Steady solver type from the dropdown menu
Denote the base file name with a marker that suggests the steady solver type
Finally, click Add and then Save As... to manually place the Cfturbo batch file in the project folder

## Slide 8: II. Select Design Variation Parameters/Export to SMP (cont.)
If transient simulation results are desired:
  Within the Settings window, ensure Export all files is selected in the dropdown menu
  Select Solver and choose the Transient solver type from the dropdown menu
  Denote the base file name with a marker that suggests the transient solver type
Finally, click Add and then Save As... to manually place the Cfturbo batch file in the project folder

## Slide 9: III. User Modification of master.cftconf
Open the project folder within the text editor and select the master.cftconf file

## Slide 10: III. User Modification of master.cftconf (Cont.)
Under [Project]:
  Assign the project name to project_name
    This should be consistent with the base file name used previously
Under [DesignVariation]:
  Set run_design_variation_bool to True
Under [Simerics]:
  Set run_simerics_bool to True

## Slide 11: III. User Modification of master.cftconf (Cont.)
Under [Steady]:
  Set avg_window to an appropriate integer value for averaging of iterations
Under [Transient]:
  Set run_transient_bool to True or False
  Set avg_window to an appropriate integer value for averaging of timesteps

## Slide 12: III. User Modification of master.cftconf (Cont.)
Under [PerformanceMap]:
  Set run_performance_map_bool to False

## Slide 13: IV. Run master.py in VS Code
Within the text editor, open terminal and run the master.py
If using Visual Studio Code:
  Select Terminal > New Terminal
  Within the terminal type python master.py and click Enter on keyboard
  Use the pip3 install [library] command to install the necessary libraries
The user is prompted to input information regarding subsecting control volumes within the flow path:
  How many subsecting CVs they wish to examine
  The number associated with the initial/final component of each subsecting CV

## Slide 14: V. Fill in Design Parameter Values in .csv
Once python master.py is executed and the subsecting control volumes are defined, the user will be prompted to fill a resultant .csv file with respective values
Once done filling the .csv file with design parameter values, return to the Terminal and press <Enter>

## Slide 15: VI. Open Results .csv File for Post-Processing
Manual convergence control can be analyzed simultaneously within the SimericsMP application
Wait for the program to finish
Within File Explorer, open the resultant .csv files
The averaged results of performance characteristics for each Cfturbo design are displayed
  The user should examine the performance of each design and run the following performance map script for the optimal design

## Slide 16: Design Variation + Performance Map Using SMP
General Outline - Performance Map:
  Create and Prepare Project Folder
  CFturbo Design Export to SimericsMP
  User Modification of master.cftconf
  Run master.py within Visual Studio Code
  Open Results .csv File for Post-Processing

## Slide 17: I. Create and Prepare Project Folder
Create and name a project folder accordingly
Download the CFturbo python scripts from github repository and place within project folder:
  master.cftconf
  master.py
  modify_spro.py

## Slide 18: II. CFturbo Design Export to SimericsMP
After the design process within CFturbo, select Export
Under Export interfaces open CFD and select Simerics
Under Components check the design parts to include in the simulations geometry

## Slide 19: II. CFturbo Design Export to SimericsMP (Cont.)
Under Settings, ensure Export all files is selected in the dropdown menu
Select Solver and choose solver type (Steady or Transient) from the dropdown menu
  steady simulations are necessary to run transient simulations
Denote the base file name with a marker that suggests the type of simulation
1
2

## Slide 20: II. CFturbo Design Export to SimericsMP (Cont.)
Assign the project folder to the Directory
Select Export
Note: If Transient simulation results are desired, Steady simulations should be run

## Slide 21: III. User Modification of master.cftconf
Open the project folder within the text editor and select the master.cftconf file

## Slide 22: III. User Modification of master.cftconf (Cont.)
Under [Project]:
  Assign the project name to project_name
    This should be consistent with the base file name used previously
Under [DesignVariation]:
  Set run_design_variation_bool to False
Under [Simerics]:
  Set run_simerics_bool to True

## Slide 23: III. User Modification of master.cftconf (Cont.)
Under [Steady]:
  Set avg_window to an appropriate integer value for averaging
Under [Transient]:
  Set run_transient_bool to True or False
  Set avg_window to an appropriate integer value for averaging

## Slide 24: III. User Modification of master.cftconf (Cont.)
Under [PerformanceMap]:
  Set run_performance_map_bool to True
  Set rpm_type to relative or absolute
  Assign the respective values to rpm_values
  Set flowrate_type to relative or absolute
  Assign the respective values to flowrate_values

## Slide 25: IV. Run master.py in VS Code
Within the text editor, open terminal and run the master.py
If using Visual Studio Code:
  Select Terminal > New Terminal
  Within the terminal type python master.py and click Enter on keyboard
  Use the pip3 install [library] command to install the necessary libraries
The user is prompted to input information regarding subsecting control volumes within the flow path:
  How many subsecting CVs they wish to examine
  The number associated with the initial/final component of each subsecting CV

## Slide 26: V. Open Results .csv File for Post-Processing
Wait for the program to finish
Within File Explorer, open the resultant .csv files
The averaged results of performance characteristics for each design point are displayed